## Slide 1
Ultrasonic-Based
Anti-Theft Alarm System
Arduino UNO · HC-SR04 Ultrasonic Sensor · LED Indicators · Buzzer Alert
Arduino Project
Embedded Systems
Security & IoT

## Slide 2
Project Overview
02
The Ultrasonic-Based Anti-Theft Alarm System is an Arduino-powered security device that uses sound waves to detect nearby objects or intruders. When armed, it continuously measures distance — triggering a buzzer alarm and flashing red LED when anything moves within 200 cm. A green LED confirms the system is active and clear.
Arm / Disarm
Push-button toggle arms or disarms the entire system instantly
Real-Time Detection
HC-SR04 pings 20×/sec with a 200 cm detection range
Dual Alerts
1 kHz buzzer tone + flashing red LED on intrusion detection

## Slide 3
Components
03
Arduino UNO
Microcontroller
ATmega328P, 14 digital I/O pins, runs at 16 MHz. The brain of the system.
📌 Power: 5V & GND
HC-SR04
Ultrasonic Sensor
Sends 40 kHz pulses; measures echo return time to calculate distance (2–400 cm).
📌 TRIG→D7, ECHO→D6
Buzzer (Passive)
Audio Alert
Piezoelectric buzzer driven by tone() at 1000 Hz when an intruder is detected.
📌 Signal→D12
Red LED + 330Ω
Visual Alert
Flashes at 200 ms intervals when armed and an object enters the detection zone.
📌 Anode→D11
Green LED + 330Ω
Status Indicator
Stays solid ON when the system is armed and no threat is detected.
📌 Anode→D10
Push Button
Arm/Disarm Toggle
Connected with INPUT_PULLUP. Single press toggles system state; 300 ms debounce.
📌 Signal→D2

## Slide 4
Circuit & Wiring
04
Component
Arduino Pin
Wire Color
HC-SR04 VCC
5V
Red
HC-SR04 GND
GND
Black
HC-SR04 TRIG
D7
Yellow
HC-SR04 ECHO
D6
Green
Buzzer (+)
D12
Purple
Red LED (+)
D11 via 330Ω
Red
Green LED (+)
D10 via 330Ω
Green
Button Pin 1
D2
Orange
Button Pin 2
GND
Black
330Ω Resistors
Each LED must use a 330 Ω resistor in series to limit current to ~10 mA and protect the Arduino pin.
INPUT_PULLUP
Button uses internal pull-up; LOW = pressed. Eliminates need for external resistor.
Breadboard GND
All GND connections share the breadboard rail tied to Arduino GND.

## Slide 5
Schematic Diagram
05
Arduino UNO
HC-SR04 Sensor
Buzzer
LEDs + Resistors
Made with Tinkercad® — Super Bruticus · 18/04/2026

## Slide 6
How It Works
08
1
Button Press
User presses button → systemArmed toggles. 300 ms debounce prevents double-trigger.
2
Ultrasonic Ping
TRIG goes HIGH for 10 µs → sensor fires 8 x 40 kHz pulses toward target.
3
Echo Timing
pulseIn() measures how long ECHO stays HIGH (µs). Speed of sound = 0.0343 cm/µs.
4
Distance Calc
distance = duration × 0.0343 ÷ 2. Divides by 2 because pulse travels TO object and back.
5
Threat Check
If distance < 100 cm → tone(buzzer,1000) + red LED flash. Else → green LED on, silence.

## Slide 7
Code Walkthrough
06
sketch.ino
#define trig 7 echo 6 buzzer 12
#define greenLED 10 redLED 11 button 2
bool systemArmed = false;
void setup() {
pinMode(trig, OUTPUT);
pinMode(echo, INPUT);
pinMode(buzzer, OUTPUT);
pinMode(greenLED, OUTPUT);
pinMode(redLED, OUTPUT);
pinMode(button, INPUT_PULLUP);
}
void loop() {
// Toggle system ON/OFF when button pressed
if (digitalRead(button) == LOW) {
systemArmed = !systemArmed; // switch state
delay(300); // debounce delay
}

## Slide 8
Summary & Upgrades
07
What We Built
Arduino UNO as the central controller
HC-SR04 sensor measuring distance in real-time
Button to toggle armed / disarmed state
Red LED + buzzer for intrusion alert
Green LED for armed + clear confirmation
Resistor-protected LEDs for circuit safety
Clean loop() with no blocking beyond debounce
Circuit Diagram